## Slide 1: Coordination between TSOs and DSOs – a necessity for system planning and operation
Dr. Ralph Pfeiffer
Amprion GmbH
PFEIFFER – DE – RT.5b

## Slide 2: Content
Characteristics of Grid Planning
Market-based Planning process
Coordination for secure system operation
Technical and economical benefits of Coordinated Planning

## Slide 3
Top-down process in a static environment
Dispatchable generation mainly on the transmission level
Generation on distribution level often not significant
Load and exchanges well predictable by TSOs and DSOs
Dimensioning planning cases could easily be determined
Characteristics of Grid Planning in the past

## Slide 4
Volatile market environment with generation dispatch driven by market economics
Dispatchable generation on transmission and distribution level
Rapidly evolving non-dispatchable generation on transmission and distribution level (on- and offshore wind, photovoltaics, …)
Demand and, in particular, cross-border exchanges hardly predictable by TSOs
Development of planning-cases requires intense exchange of information between TSOs and DSOs
Characteristics of Grid Planning today and in future

## Slide 5: Market-based Grid Planning Process
Market analysis
Generation and demand portfolio
Time-series of market-based generation dispatch including (non-dispatchable) renewable generation
Planning cases
Criteria for relevant planning cases
Transmission characteristics (transmission distances, …)
Grid analysis
Load-flow and short-circuit calculations for base-case and contingency analysis
System stability analysis by dynamic studies
Supply characteristics (peak-load, …)
Time-series of demand including imports/exports
Determination of grid reinforcements

## Slide 6: Coordination for secure system operation
From a systems engineering approach the transmission and distribution systems and their users (generators, DSOs and end-consumers) need to be considered.
Close cooperation of TSOs, DSOs and system users in normal and disturbed operating conditions is a prerequisite for secure system operation.
The behaviour of all system-users needs to be robust against perturbations and appropriate in normal and disturbed operation-conditions in order to preserve or to re-establish system security.
In particular generating units on all levels play an important role because of their ability to provide ancillary services and to operate stably in disturbed operating conditions.

## Slide 7: Why are requirements for generators so important?
Generating units connected to the transmission and distribution systems shall provide contribution to supply ancillary services to:
  Preserve system security and
  Improve system adequacy
Objectives of requirements for generating units:
  Provision of information for system management
  System balancing / frequency stability
  Voltage stability
  Robustness of generating units against perturbations (stable operation)
  System restoration after a disturbance

## Slide 8: Requirements for other customers
DSOs and end consumers
  Preservation of system security by load shedding
  Contribution to voltage stability by limiting and/or compensating reactive power consumption
DSOs
  transfer of TSO-requirements relevant for system security for generation units and end consumers connected to the distribution grid
  Communication and information exchange between TSOs and DSOs
End consumers
  Preservation of supply quality by limiting emissions like (inter-)harmonics and/ or flicker

## Slide 9: Need for common standards - keypoints
Analysis of large-scale disturbances (e. g. Nov., 4th, 2006) revealed that compatible requirements relevant for system security are strongly desirable on transmission and disribution level
Coordinated actions of TSOs and DSOs
Requirements for distribution system users (including entitlements to TSOs) gain significance for system security, in particular due to the emerging number of dispersed generation units

## Slide 10
TSOs need to expand transmission capacity
  Facilitating the internal European electricity market
  Integration of renewable energy sources
DSOs need to replace/ refurbish existing lines
  Integration of renewable energy sources
  Ageing structure of distribution grids
Initial situation for TSOs and DSOs

## Slide 11
New lines are cost-intense
Public opposition is strong
Permission procedures are time consuming
New routes are demanding to find due to
  Visual impact
  Protected areas
  Existing buildings
Restrictions for new lines

## Slide 12
Solution: combining new routes
TSO
DSO
TSO & DSO
380kV
110kV
110kV
380kV

## Slide 13
Regions with limited availability for new routes
  Only common TSO+DSO-routes may be feasible
  Permissions under public and private law may be easier to achieve
Less environmental impact
Distances to buildings etc. can be kept
Lower costs for maintenance of lines and routes
Solution: combining new routes

## Slide 14
380 kV
110 kV
120 MVA
120 MVA
120 MVA
120 MVA
120 MVA
120 MVA
ratings:
200 MVA
100 MVA
Load
Transformer
110-kV-line
Coordinated planning for optimized grid structures
EXAMPLE
Load

## Slide 15
Distributed locations of transformers enhances the reliability and robustness of supply:
  Risk of loss of supply due to out-of-range-contingencies is minimized
  Substation-blackouts have less influence
  Common-mode failures of lines have less influence
  Loss of supply can be limited locally
Improved security of supply

## Slide 16
Distributed locations of transformers enhances the quality of supply:
  In particular in rural areas with long supply distances the voltage profile of the distribution grid is evened
  Evened power flow in the distribution grid
  Reduced losses in the distribution grid
Improved quality of supply

## Slide 17
Common planning of TSOs and DSOs results in technical and economical benefits:
  Optimized transformer capacity between transmission and distribution grid
  less lines in the distribution grid
  substations with less complex/ expensive design
Economical benefits for customers
  Less equipment  less expenses  lower system usage tariffs
Economical benefits

## Slide 18
Summary
TSO/DSO coordination and cooperation is essential for
  Efficient planning processes
  Secure system operation
Coordinated planning provides
  Technical benefits
    improved security and quality of supply
    Optimized grid structures
  Cost benefits
    Combined lines
    Efficient use of assets (e.g. transformer capacities)
    Cost efficiencies

## Slide 19
Substation layout I
Transformer
overhead line
circuit breaker
disconnector
busbar

## Slide 20
Substation layout II
Transformer
circuit breaker
disconnector
busbar
overhead line